# Competency Theory – Stockpile Awareness & Training PART 2 ANSWERS

| Qual imparted | DSL THEORY D3 Stockpile Management | Qual number | N/A |
| --- | --- | --- | --- |
| Site completed | ( Lake MacLeod | ( Dampier | ( Port Hedland |
| Candidate’s name |  | SAP number |  |
| Competent content expert (if applicable) |  | SAP number |  |
| Assessor/trainer’s name |  | SAP number |  |
| Start time |  | Finish time |  |
| Relevant criteria - please tick relevant answer |
| Stockpile Awareness & Training PART 2 power point presentation reviewed by candidate | ( YES | ( NO |
| Operation manual (XX-INF-XXXX) reviewed by candidate | ( YES | ( NO |
| Has the candidate been deemed competent | ( YES | ( NO |
| Assessor/trainer comments: |
| Acknowledgement of candidate - please tick relevant answer |
| I understand & agree with the final assessment & the above comments | ( YES | ( NO |
| If NO – please comment: |
| Candidate signature |  | Date: |
| Competent content expert (if applicable) |  | Date: |
| Assessor/trainer signature |  | Date: |
| Supervisor name & signature |  | Date: |

Please email completed form to: dsltraining@riotinto.com

Guidelines - the following apply to this assessment;

- This is an open book assessment.  You are permitted and encouraged to use appropriate tools, i.e. power-point presentation, operation manual, to assist in completing,

- All questions are to be answered correctly for competency to be achieved.  If you are unsure of a question or answer request assistance from your trainer/assessor,

- There is no time limit assigned to the theory assessment,

- Please ensure written answers are legible,

- Upon completion, assessment will need to be reviewed by your trainer/assessor,

- Ensure all sections are completed before submitting.

| Question | Identify types of changes you might observe for each situation below, that might require a decision to be made related to stockpile management: (Write your answers below) |
| --- | --- |
| Answer | A change in: 1. The environment – wind – dust, stockpile conveyor (ok to stop it if wind is excessive) rain – scouring, sinking, heat – change in material handling 2. Machinery – positioning, parking (wet material may hold but not when drying out therefore parking a machinery near a stockpile when wet could present a danger when the material dries out) 3. Product – size of particles (fine vs coarse), moisture content, type of product as they behave differently, hazard of material to human contact 4. Stockpile – Angle of repose (what to do if unsure), layout of material (impact and cost of allowing stockpile to get outside of design criteria) |
| Question | Where can you find access to appropriate DSL Stockpile Management resources and list 2 specific resources available. (Write the answer) Saltnet. Find a Stockpile Plan, D3 Committee, Awareness Package for the Team, Related Standards _________________________________________________________ _________________________________________________________ |
| Answer |  |
| Question | List 4 general things related to stockpile management areas you would check during a daily shift inspection: (Write the answer) |
| Answer | 1. Inspecting the work area in general for any unsafe conditions 2. Inspecting haul road conditions and drainage 3. Inspecting Crystallizer floors and ramps 4. Stockpile size, dozing requirements, material, behaviour, working face, etc 5. Looking for unusual or out of the norm situations. 6. Identifying potential risks and hazards 7. Looking for opportunities for improvements. 8. Ensuring that the inspections conducted are diarised, dated and time referenced and available for Inspectors upon request. 9. Other works or other personnel /contractors sharing your work area that may impact your works (traffic management) _____________________________________________________________ 2. _____________________________________________________________ 3. _____________________________________________________________ 4. _____________________________________________________________ |
| Question | List 4 things a delegate needs to know when you are required to leave site? (Write answers below) |
| Answer | 1. The delegate will need to know:- How long you will be away – from to when, Who can they call if a situation arises for help or guidance What are the potential issues likely to arise during your absence What is the work that needs to be carried out, and how to confirm the competency of team members for that type of work. What are the potential or known hazards within the work area Any other relevant information for the task _____________________________________________________________ 2. _____________________________________________________________ 3. _____________________________________________________________ 4. _____________________________________________________________ |
| Question | The WHS Act requires: immediate notification of a 'notifiable incident' to the regulator after becoming aware of it? (Is this statement True or False – select the correct response) |
| Answer | True ( False ( |
| Question | You are operating a 992 Loader and working a 10 metre face, where do you think the toe will be if the face collapses? (Show your workings) |
| Answer | ________________________________________________________________ Answer 1.6 x 10m = 16m ________________________________________________________________ ________________________________________________________________ ________________________________________________________________ |
| Question | If you are standing 4 metres from the base or toe of the stockpile and a 4m x 3m x 4m section collapses. How much material in tonnes is coming your way? (assume weight per cubic metre is 1.2 tonne) (Select closest answer) |
| Answer | 10 - 15 tonnes ( 25 – 30 tonnes ( 50 - 100 tonnes ( 100 - 150 tonnes ( Approximately 60 tonnes |
| Question | It is one of your responsibilities as a Supervisor to train and help your team and Occupational Health and Safety Representative to fulfill their role in identifying Stockpile hazards? (Is this statement True or False – select the correct response) |
| Answer | True ( False ( |
| Question | The fall or release from a height of any plant, substance and/or the collapse or failure of an excavation or of any shoring supporting an excavation, is a notifiable event? (Is this statement True or False – select the correct response) |

| Answer | True ( False ( |
| --- | --- |
| Question | What would you do if you were unsure of the normal angle of a stockpile?: (Select one or more correct responses) |
| Answer | Refer to the design criteria for that stockpile ( Check angle utilising technology such as an inclinometer app. ( Not important so ignore the angle ( Seek information from someone who knows the correct angle ( |
| Question | Explain the following terms? (Write responses below) |
| Answer | Angle of Repose The maximum slope measured in degrees from the horizontal, at which loose solid material will remain in place without sliding or slumping ____________________________________________________________ Working Face The location of the stockpile from which material is being removed for transportation ________________________________________________________________ Working Height The allowable height of the working face permitted to be operated. The height is defined as the top of the machines cabin roof of the machine being utilised. _______________________________________________________________ Engulfment If the working face should collapse there is a potential for persons or equipment to be burird (engilfed) under the fallen material ______________________________________________________________ |
| Question | What would you do in the event of a stockpile incident? (Select one or more correct responses) |
| Answer | Call for assistance and report the situation ( Determine the hazards and provide this information to rescue teams ( Barricade if necessary ( Wait for support to arrive - attend to injured and monitor risks ( |
| Question | A principle task of all supervisory personnel in relation to Stockpile Management is Risk Management, a continuous non-stop activity with a need to: - continuously monitor your stockpile areas during your shift looking for potential or developing hazards and abnormal ocurances. - observe your team and others at work in your stockpile areas looking for what they are actually doing & for potential risks. - keep written records of observations and complete reports as required. (Is this statement True or False – select the correct response) True ( False ( |
| Question | For the situation below indicate what decision for action you would take as a Supervisor and explain why? Answers will vary depending on responses but should include having the operator cease work and move from the area on the basis that face above cab is too high, and that a safe working height is not being adhered (should not exceed top of cabin.The resultant fall would result in engulfment and the toe potentially exceeding the length of the loader. Incident report and other DSL procedures should be mentioned as a actions taken as a result of this observation. ________________________________________________________________ ________________________________________________________________ ________________________________________________________________ ________________________________________________________________ |

# Attach the following Practical Assessment Documents:

# ( Completed Shift Log

( Completed Monitoring Inspection Checklist

( Completed Ground Failure Report Form

# END