Resources required: Fully equipped Training Room including facilities for viewing Power-point presentation. Power Point Presentation - Stockpile Management - Supervisor Awareness & Training Part 2 v2 Power Point participant handouts are printed - one for each participant (3 slides per page) Assessment documents for this session and pens Refreshments if required Vehicles fuelled & suitable to transport the number of participants to areas for visual inspection - practical stockpile inspection. Ensure relevant permissions/permits/authorisations are in place for practical activity. Appropriate and sufficient PPE Computer and Network access to be able to access Saltnet section D3 Management of pits, slopes, stockpiles and waste dumps. Introduction: SLIDE 1: General welcome Introduction: self & participants Housekeeping: Ensure DSL attendance sheets are signed Evacuation/Muster Point Location of Fire Extinguisher Toilets Smoking areas Meals & Breaks Training times & venue 7:00am - 5:00pm CHECK FOR YOUR SITE (includes a practical component - site stockpile area inspection) - Times and breaks are indicative only and will vary upon size and make up of groups and distance to practical activity site.. Short Assessment at end of session SLIDE 2: Purpose of Training - As per the slide...highlight what Stockpile Management includes and emphasize "If it doesn't look right, then stop, think and take action". SLIDE 3: Outline for this training session - As per the slide. Discussion Starter; Dozer Incident 19th March 2006 15:45 : Operator travels between feeder 7 and 8, Stops dozer due to limited visibility. After 3 to 5 minutes of being stopped, dozer falls into feeder cone. 15:50 : Emergency signal received, Dispatch unable to verify with TRD 326, Supervisor asked to investigate 16:00 : Supervisor unable to locate Dozer, decision is made to stop the systems ( trippers and feeders). 16:10 : Mine rescue group informed. 16:20 : Excavation commences on Feeder 1 18:00 : Upper Portion of Ripper exposed in Feeder 8 20:42 : The rear window of the bulldozer is cleaned by rescue teams, who discover by way of signals that the operator is alive. 20:45 : Operator leaves the cabin of bulldozer 326 walking unaided. Cabin of dozer where operator was trapped, it is believed that the air conditioning fan continued to circulate air from engine bay through cabin throughout event Operator remained calm throughout event No additional oxygen supplies used Discuss what could have been the outcome?, What are the contributing factors?, What could have been done to prevent this incident from a Management perspective. SLIDE 4: Experiences related to stockpile incidents - Talk of experiences that either the presenter and or participants have experienced in relation to stockpile hazards & the resultant outcomes of such hazards: Responses could include experiences related to hazards of working stockpiles and dumps related to: a. engulfment b. nature of material being stockpiled or dumped c. configuration and placement of the stockpile or dump d. mobile equipment being used e. the immediate and overhead environment f. the degree of moisture and drainage of the stockpile or dump g. the method of material retrieval These hazards can result in vehicles colliding, going over the face, slipping down subsided edges, rolling over, contacting power lines, getting buried, - engulfment or any combination of these. SLIDES 5 - 11: Key definitions Commence key definition slides; Highlight to participants the importance of having the same terminology and understandings across all DSL sites. SLIDE 12: Stock Yard Boundaries - Discuss the questions highlighted in the slide. SLIDE 13: Training and Supervision - the know how! - Briefly remind how Appointed person responsibilities fit with Mines Act (s32, s33, s37, & s44 requirements), regulations, role description & importance of communication within their role. Discuss questions on highlighted on slide: Potential answers: Answer 1 - Managers, Superintendents and Supervisors need to be aware of the training and development needs of their direct reports and to implement DSL Development and Training procedure TK-PRO-1056 . Managers and Supervisors shall not permit employees to carry out work that they are not competent to carry out or where their training records do not show their current competency. Answer 2 – Changes observed: In the environment – wind – dust, stockpile conveyor (ok to stop it if wind is excessive) rain – gouging, sinking, heat – change in material handling Machinery – positioning, parking (wet material may hold but not when drying out therefore parking a machinery near a stockpile when wet could present a danger when the material dries out) Product – size of particles (fine vs coarse), moisture content, type of product as they behave differently, hazard of material to human contact Change in stockpile – Angle of repose (what to do if unsure), layout of material (impact and cost of allowing stockpile to get outside of design criteria) SLIDE 14: Supervisor responsibilities & accountability - Discuss what it means to be an S44 person in relation to management of Stockpiles. Work through slides highlighting the bolded sections of text and discussing the questions as they are indicated in the slides. In SLIDE 18 make special mention of the importance of authorisations in terms of EPA approvals and lease requirements (designated stockpile boundaries, containment of material and spillages). Have a discussion around what participants think their responsibilities are in relation to stockpile management, followed by what they think their accountabilities are. Affirm and add to the responses as required. Responses might include: Key Drivers for Responsibility and accountability: Comply with Mines Acts , regulations & Codes of Practice Risk management Regular inspections of stockpile activity Facilitation of WHS roles & representative functions Make sure employees are adequately trained & supervised Ensuring that the requirements of D3 Management Plans are met Delegation of responsibilities in a safe & appropriate way Be aware of what is normal with stockpiles and what might be abnormal signs or risk indicators. Monitoring & reporting the activities related to stockpile management Accountabilities: Accountable as an S44 Appointed person - appointed to act on behalf of Mine Manager in a particular role Legal & ethical accountability Accountable for the safety of all activity related to stockpile management. Accountable for contract staff involved in stockpile management Recording of incidents & occurrences in writing Accountable for actions and inactions of others for stockpile breaches SLIDE 15: Workplace Inspections - what is required? - Work through slides especially the highlighted questions to be asked. Take responses, affirm and add as required. SLIDE 16: Supervisor resources - indicate that there are resources are available on SaltNet to support Supervisors and that they will be a tour of this after the next slide. SLIDE 17: Shift Inspections - what is required? - Highlight the importance of Shift Inspections and the need to know what the people they are responsible for are actually doing! Highlight and discuss the areas of inspection required by working through the dot points on the slide. Utilise the LINK button to refer to Site Inspection Checklists MORNING TEA NOTE: During break, ensure link and internet connection is working! SLIDE 18: Workplace Inspections - what is required? - Give participants a guided tour of SaltNet resources available in relation to Stockpile Management SLIDE 19: Workplace Inspections - what is required? Refer to the PHOTO indicating how quickly things can change. Indicate that at the start of the inspection the weather was fine and this is what we headed into after about half an hour. Answer to Question 1 – Refer to Design Criteria and/or ask someone who knows. Utilise LINK button to demonstrate an inclinometer app or utilise a phone with suitable app installed to demonstrate how to measure angle of stockpile. Answer to Question 2 – Cost of managing the product can be increased, Machinery reliability can be affected, Increase cost of creating a stock yard if angle of repose is incorrectly determined. SLIDE 20: Reporting - leads to prevention & mitigation - Highlight the importance of reporting and take responses from participants of the kinds of Stockpile Management occurrences they would see as necessary to report? Responses may include: Breaches related to stockpile boundaries Machinery and operator incidents especially around angle of repose Spillages, dust, contamination Abnormalities sighted that might have been missed in risk assessments - potential slumping, rock falls, engulfment Non compliance with DSL procedures and systems Utilise LINK buttons to demonstrate the reporting forms utilised related to: 1. Crystalliser Floor Failure 2. Ground, earthen structure and stockpile failure SLIDES 21: Risk Mitigation - Work through the slides asking the initial question of the risk that can be identified in the first picture, the tools to be utilised for reporting and then show participants how this risk was mitigated through remaining pictures. What can you do as a means to managing risk? ANSWER: CRM Inspections. What is the highest risk activity related to stockpiles? ANSWER: Sampling of stockpiles Question? – What other risks may require management? ANSWER: Take responses from participating Supervisors, eg. weather conditions (wind), survey work, placement of leaching lines (LM) SLIDES 22-26: Risk Management - Work through slides depicting an example of a risk identified and its subsequent mitigation to manage risk. Ask highlighted question on Slide 24 and take responses including the need to inspect to ensure drainage provisions embedded in the face are working, cracking and moving etc. Outline the study findings of fifty two detailed investigation reports highlighting the areas in RED (Slide 25) and then the identified latent conditions considered important factors for Supervisors to recognise. Discuss the question highlighted at the end of SLIDE 26. SLIDES 27- 30: Risk Management Incident - Work through typical stockpile incidents on the slides or if applicable a DSL example if appropriate. SLIDE 31: PRACTICAL ACTIVITY - Stockpile area tour and inspection - it is expected that a real inspection of stockpile areas will be undertaken utilising appropriate inspection checklists/tools etc. LUNCH SLIDES 32-33: Compliance - Utilise highlighted questions to discuss the importance and need for compliance. Highlight the human factor cost if there is non-compliance. SLIDE 34: Risk Scenario 1 - Highlight the need to be diligent in risk identification, mitigation and compliance. The question could be asked, "Have you met with a DMP Inspector in relation to an incident, and what was it like?" Supervisors are responsible for things incidents such as: the collapse or partial collapse of a structure the collapse or failure of an excavation or of any shoring supporting an excavation the inrush of water, mud or gas in workings, in an underground excavation or tunnel, or the interruption of the main system of ventilation in an underground excavation or tunnel. SLIDE 35: Risk Scenario 2 - Discuss how with the Supervisors how they would manage this incident. Include in the discussion who they would communicate with and what information they would provide. SLIDES 36: Statutory compliance - reiterate the Supervisor's responsibilities as indicated on the slide and the need for compliance in terms of seeking approvals, reporting, Codes etc. Ask the key question highlighted on the slide. CLICK to get ANSWER: Because they have been written in blood. SLIDE 37: Delegation of your responsibilities - Discuss the question highlighted in the slide and discuss the importance of delegation and how this is occurring now and how it might be improved. SLIDE 38 - 41: Slippages, and collapse, - bare facts & putting force into perspective - Work through slides highlighting Angle of Repose, how to calculate slippage and the impact likely. At slide 39, highlight that the material will fall further that the length of a 992 Loader eg. 10 x 1.6 = 16metres. Length of loader with bucket on the ground is approximately 15 metres. Slide 41 has links to relevant news items for discussion. There is also a LINK button that refers to key slide from Part 1 training related to how our material behaves. SLIDES 42: Work through questions highlighted in slide. Discuss rescue verses recovery - the need to take notice and ensure other stakeholders are aware of potential further risk - engulfment could be used a example in developing guidelines. Answer to Question 1 may include: Engulfment Contact with Lime waste – even when washing down machinery - (has it got reactive/corrosive waste in it)? Sinking of soft waste eg. Gypsum, Answer to Question 2 may include: Engulfment – prevent others from being engulfed, barricade, describe the product and characteristics to the rescue team. Lime Waste – Treat as a hazard: Warn of the corrosiveness when operating, even when exiting machine and/ or washing the machine and equipment, make sure operator’s of machinery and rescue teams are aware of the corrosive nature of product and take suitable PPE & procedures to mitigate risk (MHS) SLIDES 43-44: Emergency management - Outline the things to be considered when planning controls - work through content of slides. SLIDE 45: Our challenge - recap - highlight the difference between experience of time versus understanding what we are seeing and doing as a practice. Seek from participants a few things that they have learned as a result of the training and what they will change when returning to work in their Supervisory role in terms of Stockpile Management. Take any questions the participants might have. SLIDE 46: Written Assessment SLIDE 57: Conclude with asking participants what they will take away from the training session and what they will do differently. Complete feedback sheets if applicable. Thank participants for attendance & participation.

END